# MODEL DOCUMENT #11:

## SAMPLE OF A

## LEAD-BASED PAINT HAZARD

## RISK ASSESSMENT REPORT

FOR THE DWELLING LOCATED AT:

123 Main Street

Anytown, USA 12345

PREPARED FOR:

Mr. Joseph Smith, Owner

987 South Street

Anytown, USA 12345

BY:

John Doe, Certified Risk Assessor

456 North Street

Anytown, USA 12345

Any State License No:  00-567

Table of Contents

Part I: Identifying Information

1.	Risk Assessor, Name of Certificate (or License) and Number and State issuing certificate/license.

2.	Property Owner Name, Address, and Phone Number.

3.	Date of Report, Date of Environmental Sampling.

Part II: Completed Management, Maintenance, and Environmental Results Forms and

Analyses

1.	List of Location and Type of Identified Lead Hazards including an indication of which hazards are priorities (this summary should be suitable for use as notification to residents).

2.	Optional Management Information (Form 5.6) (not required for homeowners).

3.	Maintenance/Paint Condition Information (Form 5.2 or 5.7).

4.	Building Condition (Form 5.1).

5.	Brief Narrative Description of Dwelling Selection Process (not required if all dwellings were sampled).

6.	Analysis of Previous XRF Testing Report (if applicable).

7.	Deteriorated Paint Sampling Results (Form 5.3 or 5.3a).

8.	Dust Sampling Results (Form 5.4 or 5.4a).

9.	Soil Sampling Results (Form 5.5).

10.	Other Sampling Results (if applicable).

Part III: Lead Hazard Control Plan

1.	Lead-Based Paint Policy Statement (not applicable for homeowners).

2.	Name of Individual in Charge of Lead-Based Paint Hazard Control Program.

3.	Recommended Changes to Work Order System and Property Management (optional, not applicable for homeowners or property owners without work order systems).

4.	Acceptable Interim Control Options For This Property and Estimated Costs.

5.	Acceptable Abatement Options For This Property and Estimated Costs.

6.	Reevaluation Schedule (if applicable).

7.	Interim Control/Abatement to Be Implemented in This Property.

8.	A Training Plan for Managers, Maintenance Supervisors, and Workers (this should include named individuals), if applicable.

9.	Method of Resident Notification of Results of Risk Assessment and Lead Hazard Control Program (not applicable for homeowners). Note: This section should include a discussion of how residents are to be educated about lead poisoning, before the risk assessment results are released.

10.	Signatures (Risk Assessor) and Date.

Part IV: Appendix

1.	All laboratory raw data.

#### Part 1: Identifying Information

A lead-based paint risk assessment was conducted at 123 Main St. in Anytown, USA

12345 for Mr. Joseph Smith, Owner, who is located at 987 South Street, Anytown, USA 12345 (400-777-7777) on April 1, 2000.  The risk assessment was conducted by John Doe, a Certified Risk Assessor (Any State License No. 00-567).

Part II: Completed Management, Maintenance and Environmental Results, Forms and Analyses

1.		List of Location and Type of Identified Lead Hazards

While the building and its paint are in reasonably good condition overall, the risk

Assessment showed that lead-based paint hazards (as defined in Title X of the 1992 Housing and Community Development Act) exist in the following locations:

a.	Deteriorated lead-based paint on the exterior side of the windows.

b.	Leaded dust on the floor of Bobby’s bedroom (the southeast bedroom on the second floor).

c.	Deteriorated lead-based paint on the interior door leading to Bobby’s bedroom (the southeast bedroom

A few other painted surfaces that have not been tested for lead are in “fair” condition and should be repainted within the next year before further deterioration occurs.  However, these surfaces are not considered to be immediate “hazards,” using criteria in the 1995 HUD Guidelines for the Evaluation and Control of Lead-Based Paint Hazards in Housing.  Those surfaces are:

Exterior Doors;

Exterior Railings;

All Interior Doors (except the bedroom door to the southeast bedroom, which is in poor

condition and requires repair immediately);

Interior window trim;

Stairways; and

Bathroom cabinets.

Since vacancies occur frequently in this property, these surfaces can be repainted at that time. Before any scraping or sanding, the paint should be tested to see if it contains lead.  The paint on the porch floor is in poor condition, but since it does not contain lead-based paint, it does not require priority attention.

There has not been any previous lead-based paint testing at this dwelling, although a lead-based paint inspection of all painted surfaces is recommended so that potential lead problems can be monitored before they become hazardous.  Soil lead levels were all below 400 µg/g. Current EPA and HUD Guidance for soil is 400 µg/g for bare play areas and 2,000 µg/g for other areas.  Using these criteria, soil is not a hazard at this property.

The owner has decided to select the following hazard control measures, which are all acceptable based on HUD’s Guidelines for the Evaluation and Control of Lead-Based Paint Hazards in Housing:

- stabilize the paint on the exterior of all the windows;

- remove the lead dust located in the child’s bedroom; and

- replace the door leading to the southeast second floor bedroom.

Mr. Smith has chosen to use interim controls for the windows until 2003, when the State of Any State is likely to begin a special loan fund for financing lead-based paint abatement that should make window replacement financially possible.  Mr. Smith will also make sure that the part-time as-needed maintenance worker he uses will be trained.  Certain property management practices will be adopted to ensure that the normal repair work done will not disturb those surfaces with lead-based paint.

After the cleaning and paint film stabilization work has been completed, clearance dust samples must be taken to make certain that the dwelling is lead-safe before the family moves back in to the room.

Reevaluation:  Standard Reevaluation Schedule 3 contained in the HUD Guidelines applies to this property, since one of the rooms had a dust lead level greater than the standard. Therefore, the dwelling should be reevaluated in April 2001 (12 months from now).  If no lead-based paint hazards are identified at that time, another reevaluation should be conducted in April 2003 (2 years later).  If no lead-based paint hazards are identified at that time, no further reevaluations are needed.  However, since lead-based paint may be present in the dwelling, the owner should monitor the condition of all painted surfaces at least annually or whenever other information indicates a potential problem.

Mr. Smith has agreed to share the results of this report with the Jones family, which now occupies the residence and to provide the family with the EPA brochure and a brochure from the Anytown Childhood Lead Poisoning Prevention Program as a way of educating the residents.

Form 5.0

Resident Questionnaire (Optional)

### Children/Children’s Habits

1.	(a)  Do you have any children that live in your home?  Yes __x__  No ___

(b)  If yes, how many?  __2__ Ages? __1__ __3__ _

(c)  Record blood lead levels, if known   ____ ____ ____ ____ ____ _____

IF NO CHILDREN, SKIP TO Q.5

2.	Locate the rooms/areas where each child sleeps, eats and plays.

| Name of Child | Location of Bedroom | Location of all rooms where child eats | Primary location where child plays indoors | Primary location where child plays outdoors |
| --- | --- | --- | --- | --- |
| Bobby | Southeast – Second floor | Kitchen | Living Room | Back yard under jungle gym |
| Jennifer | South west – Second floor | Kitchen | Living room | Back yard under jungle gym |

3.	Where are toys stored/kept? ____ Living room __________________

4.	Is there any visible evidence of chewed or peeling paint on the woodwork, furniture or toys?  Yes _____   No ____

#### Family Use Patterns

5.	Which entrances are used most frequently? ___ Front door_________

6.	Which window are opened most frequently?  ___ Living room ______

7.	Do you use window air conditioners?  If yes, where?  ___ No ________

8.	Do any household members engage in gardening?  Yes ____  No __X__

(a)  Record the location of any vegetable garden. ___ No garden __________

(b)   Are you planning any landscaping activities that will remove grass

Or ground covering?		Yes ____  No __X__

9.	How often is the housing unit cleaned?  __once/week__

(a)  What cleaning methods do you use?  __mopping and sweeping___

10.	(a)  Did you recently complete any building renovations? Yes ____  No __X__

(b)  If yes, where? ____________________

(c) Was building debris stored in the yard?  If yes, where? ________________

11.	Are you planning and building renovations?  Where? ______No_________

12.	(a)  Do any household members work in a lead-related industry? Yes ___  No __X__

(b)  If yes, where are dirty work clothes placed and cleaned? ____________

Form 5.6

Management Data for Rental Dwellings

##### Part 1:  Identifying Information

Identifying Information:

Name of Building or Development Not Applicable

Number of Buildings ______1_______

Number of Individual Dwelling Units/Building:  ____1____

Number of Total Dwelling Units:  ___1___

Date of Construction 1937 (if between 1960 – 1978, consider a lead hazard screen)

Date of Substantial Rehab, if any None

List Address of Dwellings (attach list if more than 10 dwellings are present)

| Dwelling No. | Address | No of Children Aged 0 – 6 Years Old | Recent Code Violation Report by Owner? | Chronic Maintenance Problem? |
| --- | --- | --- | --- | --- |
| 1. | 123 Main St Anytown, USA |  |  |  |

Record number and locations of common child play areas (on-site playground, backyards, etc.)

One. Play structure in back yard.

Part 2: Management Information

- List names of individuals who have responsibility for lead-based paint.  Include owner, property manager (if applicable), maintenance supervisor and staff (if applicable) and others.  Include any training in lead hazard control work (inspector, supervisor, worker, etc.) that has been completed.  Use additional pages, if necessary.

This information will be needed to devise the risk management plan contained in the risk assessor’s report.

| Name | Position | Training Completed (if none, enter “None” |
| --- | --- | --- |
| Joseph Smith | Owner | None |
| Not Applicable | Property Manager |  |
| Joe Jones | Maintenance Worker | None |

2.	Have there been previous lead-based paint evaluations?

_____Yes  __x__No (If yes, attach the report)

3.	Has there been previous lead hazard control activity?

_____Yes  __x__No (If yes, attach the report)

4.	Maintenance usually conducted at time of dwelling turnover:

Repainting____Where needed____________

Cleaning____Where needed______________

Repair____Where needed________________

- Employee and Worker Safety Plan

- Is there an occupational safety and health plan for maintenance workers?

_____Yes  __x__No     (If yes, attach plan)

- Are workers trained in lead hazard recognition?

_____Yes  __x_ No

If yes, who performed the training?__________________

- Are workers involved in a hazard communication program?

_____Yes  __x__No

- Are workers trained in property use of respirators?

_____Yes  __x__No

- Is there a medical surveillance program?

_____Yes  __x__No

- Is there a HEPA Vacuum available?

_____Yes  __x__No

- Are there any on-site licensed or unlicensed day-care facilities?

_____Yes  __x__No

If yes, give location__________________________

- Planning for Resident Children with Elevated Blood Levels

- Who would respond for the owner if a resident child with an elevated blood lead level was identified?

###### The owner

- Is there a plan to relocate such children?

_____Yes  __x__No  If yes, where?_________________________

- Do you (the owner) know if there ever has been a resident child with an elevated blood lead level?

_____Yes  _____No  __x__Unknown

- Owner Inspections

- Are there periodic inspections of all dwellings by the owner?

__x__Yes   _____No

If yes, how often?  Every year or whenever the unit is vacant.

- Is the paint condition assessed during these inspections?

__x__Yes   _____No

8.  Have any of the dwellings ever received a housing code violation notice?

_____Yes  __x__No _____Unknown

If yes, describe code violation    ___________________________

________________________________________________________

9. If previously detected, unabated lead-based paint exists in the dwelling, have the

residents been informed?__Yes  __ No  __Not Applicable

Form 5.7

Maintenance Data for Rental Dwellings

Recorded during onsite investigation

1. Condition of Paint on Selected Surfaces

| Building Component | Paint Condition (Intact, Fair, Poor or Not Present) To be Completed by Risk Assessor | Deterioration Due to Friction or Impact? | Deterioration due to Moisture? | Location of Painted Component with Visible Bite Marks |
| --- | --- | --- | --- | --- |
| Building Siding | Intact |  |  |  |
| Exterior Trim | Intact |  |  |  |
| Window Troughs | Poor | No | No |  |
| Exterior Doors | Fair | Yes | No |  |
| Railings | Fair | Yes | No |  |
| Porch Floors | Poor | Yes | No |  |
| Other Porch Surfaces | Intact |  |  |  |
| Interior Doors | Fair (Door to Southeast bedroom is poor) | Yes | No |  |
| Ceilings | Fair |  | No |  |
| Walls | Intact |  |  |  |
| Interior Windows | Fair | Yes | No |  |
| Interior Floors | Fair | Yes | No |  |
| Interior Trim | Intact |  |  |  |
| Stairways | Fair | Yes | No |  |
| Radiator (or Radiator Cover) | Intact |  |  |  |
| Kitchen cabinets | Intact |  |  |  |
| Bathroom cabinets | Fair | Yes | No |  |
| Other surfaces |  |  |  |  |

If the overall condition of a component is similar throughout a dwelling, that condition should be recorded.  If a component in a couple of locations is in poor condition but the overall condition is good or fair, the specific sites of the badly deteriorated paint should be noted.  The specific locations of any component with bite marks should be recorded.

Form 5.7 (Continued)

2. Painting Frequency and Methods

- How often is painting completed?  Every ___5___ years.

- Is painting completed upon vacancy, if necessary?

__x__Yes   ____No

- Who does the painting? __x__ Property Owner  ____Residents

- Is painting accompanied by scraping, sanding or paint removal?

__x__Yes   ____No

e.  How are paint dust/chips cleaned up? (check one)

__x__Sweeping  ____Vacuum   ____Mopping   ____HEPA/TSP/HEPA

- Is the work area sealed off during painting? ____Yes  __x__No

- Is furniture removed from the work area?  ____Yes  __x__No

- If no, is furniture covered during work with plastic?

____Yes  __x__No

3.  Is there a preventive maintenance program?

____Yes  __x__No

Describe work order system (if applicable, attach copy of work order form).  There is no formal work order system

5.	How are resident complaints received and addressed?  How are requests prioritized?  If formal work orders are issued, is the presence or potential presence of lead-based paint considered in the work instructions?

Resident complaints are received directly by the owner, who then authorizes the maintenance employee to complete the necessary repairs.  The presence of lead-based paint is not routinely considered in the repair and maintenance work.

6.   Record location of dwellings recently prepared for re-occupancy.

Not Applicable

Form 5.1

Building Condition Form

| Condition | Yes | No |
| --- | --- | --- |
| Roof missing parts of surfaces (tiles, boards, etc.) |  | X |
| Roof has holes or large cracks |  | X |
| Gutter or downspouts broken | X |  |
| Chimney masonry cracked, bricks loose or missing, obviously out of plumb |  | X |
| Exterior or interior walls have obvious large cracks or holes requiring more than routine painting |  | X |
| Exterior siding has missing boards or shingles |  | X |
| Water stains on interior walls or ceilings |  | X |
| Plaster walls deteriorated |  | X |
| Two or more windows or doors broken, missing or boarded up |  | X |
| Porch or steps have major elements broken, missing or boarded up |  | X |
| Foundation has major cracks, missing material, structural leans or visibly unsound |  | X |
| Total | 1 (see notes) |  |

If the “yes” column has 2 or more checks, the dwelling is considered to be in poor condition for the purposes of a risk assessment.  However, specific conditions and extenuating circumstances should be considered before determining final condition of the building and the appropriateness of a lead hazard screen.

Notes:

Gutter downspout reattached during visit; owner stated that it was due to a recent storm.

1.	Dwelling Selection Process

This section is not applicable for this property.

2.	Analysis of Previous XRF Testing Report

There is no previous XRF Testing Report; this section is not applicable for this property.

Form 5.3

Field Sampling Form For Deteriorated Paint

Name of Risk Assessor  	John Doe

Name of Property Owner  	Joseph Smith

Property Address	123 Main Street, Anytown, USA 12345 Apt No. ______

Sampling Protocol	__x__All Dwellings   ____Targeted  ____Worst-Case  ____Random

Target Dwelling Criteria  (Check all that apply)

____	Code Violations

____	Judged to be in Poor Condition

____	Presence of 2 or More Children between Ages of 6 Months and 6 Years

____	Serves as Day-Care Facility

____	Recently Prepared for Re-occupancy

____	Random Sampling

____	None of the above

| Sample Number | Room | Building Component | Laboratory Result (µg/g) or XRF Reading (mg/cm2) |
| --- | --- | --- | --- |
| 1 | Southeast Child’s Bedroom (Bobby’s room) | Window Trough Frame | 9.2 mg/cm2 (portable XRF) |
| 2 | Front Porch | Floor | 0.1 mg/cm2 (portable XRF) |
| 3 | Southeast Child’s Bedroom (Bobby’s room) | Interior Door | 5.3 mg/cm2 (portable XRF) |
| 4 | Living Room | Window, Trough Frame | 7.8 mg/cm2 (portable XRF) |
| HUD/EPA STANDARD |  |  | 1 mg/cm2 or 0.5% by weight |

Sample all layers of paint, not just deteriorated paint layers

Total Number of Samples This Page ___4___

Page ____1____ of ____1____

Date of Sample Collection __4/1/00__  Date Shipped to Lab __4 /1/00__

Shipped by _______________________  Received by _________________________

(Signature)					(Signature)

Date Results Reported __4/10/00__

Analyzed by __Lisa Baker___________

Approved by __Jim Zimmerman______

Form 5.4

Field Sampling Form For Dust (Single Surface)

Name of Risk Assessor  	John Doe

Name of Property Owner  	Joseph Smith

Property Address	123 Main Street, Anytown, USA 12345 Apt No. ______

Sampling Protocol	__x__All Dwellings   ____Targeted  ____Worst-Case  ____Random

Target Dwelling Criteria  (Check all that apply)

Code Violations

____	Judged to be in Poor Condition

____	Presence of 2 or More Children between Ages of 6 Months and 6 Years

____	Serves as Day-Care Facility

____	Recently Prepared for Re-occupancy

| Sample Number | Room (Record name of room used by the Owner or Resident) | Surface Type | Is Surface Smooth and Cleanable? | Dimensions1 of sample area (inches x inches) | Area (ft2) | Result of Lab Analysis (µg/ ft2) |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Play Room Living Room | Floor | Yes | 12 x 12 | 1 | 79 |
| 2 | Play Room Living Room | Interior Window Sill | Yes | 3 x 33 | 0.69 | 150 |
| 3 | Kitchen | Floor | Yes | 12 x 12 | 1 | <25 |
| 4 | Kitchen | Window Trough | No | 3 x 25 | 0.52 | 579 |
| 5 | Bedroom 1 Bobby (Southeast) | Floor | No | 12 x 12 | 1 | 1,356 |
| 6 | Bedroom 1 Bobby (Southeast) | Interior Window Sill | No | 2.5 x 34 | 0.59 | 400 |
| 7 | Bedroom 2 Jennifer (Southwest) | Floor | Yes | 12 x 12 | 1 | 29 |
| 8 | Bedroom 2 Jennifer (Southwest) | Window Trough | No | 3 x 33 | 0.69 | 600 |
| 9 | Blank |  |  |  |  | <25 |
| HUD/EPA STANDARD |  | Floor Interior window sill |  |  |  | 40 µg/ ft2 250 µg/ ft2 |

1Measure to the nearest 1/8 inch

Total Number of Samples This Page ___9___

Page         1        of      1

Date of Sample Collection    4/1//00    Date Shipped to Lab    4/4/00

Shipped by _______________________  Received by _________________________

(Signature)					(Signature)

Form 5.5

Field Sampling Form For Soil

Name of Risk Assessor  	John Doe

Name of Property Owner  	Joseph Smith

Property Address		123 Main Street, Anytown, USA 12345 Apt No. ______

| Sample Number | Location | Bare or Covered | Lab Result (µg/g) |
| --- | --- | --- | --- |
| 1 | Building Perimeter | Bare | 222 |
|  | Building Perimeter |  |  |
| 2 | Play Area 1 (describe) Back Yard Jungle Gym | Bare | 102 |
|  | Play Area 2 (describe) |  |  |

Collect only the top 1/2” of soil

Total Number of Samples This Page ___2___

Page ____1____ of ____1____

Date of Sample Collection __4/1/00__  Date Shipped to Lab __4 /1/00__

Shipped by _______________________  Received by _________________________

(Signature)					(Signature)

3.	Other Sampling Results

The owner decided not to have water sampling conducted at this property.

Part III:  Lead Hazard Control Options

1.	Lead-Based Paint Policy Statement

The owner indicated such a statement would be developed.

- Name of Individual in Charge of Lead-Based Paint Hazard Control Program:  Joseph Smith

- Recommended Changes to Work Order System and Property Management

The existing work order system is an informal, verbal one.  If painted surfaces will be disturbed during a particular repair job, the painted surface should be tested to determine if it has lead-based paint on it.  If it does (or if testing is not completed), the maintenance worker should take the necessary precautions by wetting down the surface and performing cleanup.  If the surface area is large or if the work will generate a significant amount of dust, clearance testing should be completed before residents move back into the room.  The table below can be used as a general guide in determining whether maintenance jobs are likely to be high risk or low risk.

When work is assigned, the owner or worker should determine whether or not the job is low or high risk and adopt protective measures as needed.

Table 17.1 (Taken from HUD Guidelines)

Summary of Low- and High-Risk Job Designations for Surfaces Known or Suspected to Have Lead-Based Paint

| Job Description | Low Risk | High Risk* |
| --- | --- | --- |
| Repainting (includes surface preparation) |  | √ |
| Plastering or wall repair |  | √ |
| Window repair |  | √ |
| Window pane or glass replacement only | √ |  |
| Water or moisture damage repair (repainting and plumbing) |  | √ |
| Door repair | √ |  |
| Building component replacement |  | √ |
| Welding on painted surfaces |  | √ |
| Door lock repair or replacement | √ |  |
| Electrical fixture repair | √ |  |
| Floor refinishing |  | √ |
| Carpet replacement |  | √ |
| Grounds keeping | √ |  |
| Radiator leak repair | √ |  |
| Baluster repair (metal |  | √ |
| Demolition |  | √ |

*  High-risk jobs typically disturb more than 2 square feet per room.  If these jobs disturb less than 2 square feet, then they can be considered low-risk jobs.

Table 17.2

Summary of Protective Measures for Low-Risk and High-Risk Jobs

| Protective Measure | Low Risk | High Risk |
| --- | --- | --- |
| Worksite preparation with plastic sheeting (6 mil thick) | Plastic sheeting no less than 5 feet by 5 feet immediately underneath work area | Whole floor, plus simple airlock at door or tape door shut |
| Children kept out of work area | Yes | Yes |
| Resident relocation during work | No | Yes |
| Respirators | Probably not necessary | Recommended |
| Protective clothing Note: Protective shoe coverings are not to be worn on ladders, scaffolds, etc. | Probably not necessary | Recommended |
| Personal hygiene (enforced hand washing after job) | Required | Required |
| Showers | Probably not necessary | Recommended |
| Work practices | Use wet methods, except near electrical circuits | Use wet methods, except near electrical circuits |
| Cleaning | HEPA vacuum and wet clean with suitable detergent around the work area only (2 linear feet beyond plastic) | HEPA vacuum/wet wash/HEPA vacuum the entire work area |
| Clearance | Visual examination only | Dust sampling during the preliminary phase of the maintenance program and periodically thereafter (not required for every job) |

Employers must have objective data showing that worker exposures are less than the OSHA Permissible Exposure Limit of 50µg/m3 if respirators and protective clothing will not be provided.

Paint chips are now cleaned up by sweeping.  Mopping or other wet cleaning methods should be used instead.

If residents are present, the work area should be sealed off so that leaded dust does not enter the living area.  Any furniture present should be moved or covered with plastic.  The possible presence of lead-based paint should be considered in all repair and maintenance work.

A lead-based paint inspection should be completed at some point in the future to determine exactly where all the lead-based paint is located so that it can be properly managed.

The Anytown Childhood Lead Poisoning Prevention Program offers a general awareness class in lead-based paint hazards, which both the owner and the maintenance worker should attend.  The program also offers the use of a HEPA vacuum and provides advice on respirators and medical surveillance and other lead-related issues.

The practice of examining the condition of the paint annually or upon vacancy is a good one and should be continued.

Since the paint has not yet been completely tested, it should be assumed to contain lead-based paint.  The owner should tell residents to report any paint that is peeling, chipping, flaking, chalking, or otherwise deteriorating so that it can be repaired quickly and safely.

1.	Interim Control Options and Estimated Costs

The costs shown below include labor, materials, worker protection, site containment and cleanup.  These are only very rough estimates that may not be accurate; a precise estimate should be obtained from a contractor.

Hazard A: Window Trough Surfaces

a. Paint Film Stabilization of both frame and sash		             $xx/window

b. Encapsulation of Exterior Frame with a Liquid Encapsulant Coating plus sash

replacement						             $xx/window

Hazard B: Leaded Dust On Bobby Jones’ Bedroom (Southeast Bedroom) Floor

a. Dust removal and re-coating hardwood floor with polyurethane

$xx

Hazard C:  Deteriorated Lead-Based Paint on the interior door leading to Bobby’s Bedroom (Southeast Bedroom)

a. Paint Film Stabilization plus re-hang door for smooth operation (paint film

stabilization alone without door repair is not appropriate                 $xxx

2.	Acceptable Abatement Options and Estimated Costs

Hazard A Window Trough Surfaces

a. Enclosure of window frame with metal panning system

plus sash replacement						 $xx/window

b. Replacement of entire window assembly				 $xx/window

c. Remove all lead-based paint from entire window assembly using

chemical paint removers						 $xx/window

Hazard B: Leaded Dust On Bobby’s Bedroom (Southeast Bedroom) Floor

a. Enclosure of floor with new sub-flooring and tile			$xxx/room

Hazard C: Deteriorated Lead-Based Paint on the interior door leading to Bobby’s Bedroom (Southeast Bedroom)

a. Replace door and door frame						$xxx

b. Encapsulate door							$xxx

c. Replace door and enclose door frame					$xxx

d. Remove lead-based paint from door and door frame chemically	$xxx

3.	Re-evaluation and Monitoring Schedule

Each of these treatments will need to be reexamined periodically to make certain that they remain effective and to ensure that new lead-based paint hazards do not appear.  The interim controls shown above are less expensive initially, but they may be more expensive in the long run since they need to be reevaluated more frequently.  The replacement and paint removal methods are more expensive initially, but do not require any reevaluation.

The owner should monitor the condition of the paint at least annual annually or if there is some indication that paint might be failing.

Part IV: Site-Specific Lead Hazard Control Plan

1.  Lead Hazard Control Option To Be Implemented in This Property

Hazard A: Window Trough Surfaces

Paint Film Stabilization of both frame and sash

Hazard B: Leaded Dust On Bobby Smith’s Bedroom (Southeast Bedroom) Floor

Dust removal and re-coating hardwood floor with polyurethane

Hazard C: Deteriorated Lead-Based Paint on the interior door leading to Bobby’s Bedroom (Southeast Bedroom)

Replace door and door frame

2.  Training Plan for Managers, Maintenance Supervisors and Workers

The part-time worker will attend the lead awareness class offered by the Anytown Childhood Lead Poisoning Prevention Program to learn how maintenance work can be conducted safely when dealing with lead-based paint.  The owner has agreed to attend the same class.  The Appendix to this report contains brochures with the relevant information.

3.   Method of Resident Notification of Results of Risk Assessment and Lead Hazard Control

Program

The owner will provide the summary of this report to the residents in the dwelling. The brochure in the Appendix will be provided to the residents.  The owner will explain to the resident that the lead hazards at the property will be corrected within two weeks.  The dwelling will be tested after the work has been completed to make certain that it was effective.  After the work has been completed and clearance established, a certificate will be appended to this report.

4.   Signatures (Risk Assessor and Owner), Date and Certificate of Lead-Based Paint

Compliance

________________________________

Joseph Smith, Owner

(Date)

________________________________

John Doe, Certified Risk Assessor

(Date)

##### SUMMARY OF HAZARD REDUCTION ACTIVITIES

| Name of Firm: | ABC Contracting, Inc. |
| --- | --- |
| Address of Firm | 100 River Road Anytown, USA 12345 |
| Supervisor: | Sam Jones X98765 |
| State LBP Number: | 0000 |
| Start and Completion date of hazard reduction activity or completion activity | May 1 – May 6, 2000 |

DESCRIPTION OF HAZARD REDUCTION ACTIVITIES AND AREAS ADDRESSED:

Exterior:  	Stabilization of trim, decks enclosed.

Exterior window trim enclosed.

Interior:	Standard treatments with sash replacement.

MONITORING RECOMMENDATIONS:

Exterior: Stabilized areas should be inspected yearly and all deteriorated paint repaired.

Interior:  Inspect stair components for physical damage yearly.

##### CLEARANCE EXAMINATION:

##### VISUAL INSPECTION RESULTS

Date:	May 6, 2000

LOCATION OF DEFECTS IN THE WORK AREA

|  |  | Check any that apply and indicate location |
| --- | --- | --- |
| Work Area | Pass/Fail Circle one | Deteriorated Paint | Debris | Visible Dust | Notes |
| Exterior Front Porch | Pass/Fail |  |  |  |  |
| Exterior Rear Porch | Pass/Fail |  |  |  |  |
| Foyer | Pass/Fail |  |  |  |  |
| Living Room | Pass/Fail |  |  |  |  |
| Dining Room | Pass/Fail |  |  |  |  |
| Kitchen | Pass/Fail |  |  |  |  |
| Stairwell | Pass/Fail |  |  |  |  |
| Second Floor Hallway | Pass/Fail |  |  |  |  |
| Bedroom 1 | Pass/Fail |  |  |  |  |
| Bedroom 2 | Pass/Fail |  |  |  |  |
| Bedroom 3 | Pass/Fail |  |  |  |  |
| Bathroom 1 | Pass/Fail |  |  |  |  |
| Bathroom 2 | Pass/Fail |  |  |  |  |
| Other | Pass/Fail |  |  |  |  |
| Other | Pass/Fail |  |  |  |  |

NOTE:   IF ANY DEFECTS ARE IDENTIFIED THEY MUST BE CORRECTED PRIOR TO SAMPLING FOR DUST LEAD LEVELS.

#### CLEARANCE EXAMINATION:

#### DUST SAMPLING RESULTS

Date of Collection:	May 6, 2000

| Sample | Location | Surface | Dimensions of Sample Area | Lead µg /ft2 | Above/ Below Standard |
| --- | --- | --- | --- | --- | --- |
| 2136-1 | Upstairs small bedroom #12 | Window (C-2) | 4” x 18” | 110 | Below |
| 2136-2 | Upstairs small bedroom #12 | Floor under C-1 window | 12” x 12” | 25 | Below |
| 2136-3 | Upstairs bedroom #15 | Window (C-1) | 4” x 18” | 95 | Below |
| 2136-4 | Staircase/ Landing #10 | Floor | 12” x 12” | 39 | Below |
| 2136-5 | Kitchen #7 | Floor under A-1 window | 12” x 12” | ND | Below |
| 2136-6 | Kitchen #7 | Window (A-1) sill | 4” x 18” | 160 | Below |
| 2136-7 | 1st Foyer | Floor | 12” x 12” | 30 | Below |
| 2136-8 | Blank | Blank | 12” x 12” | ND | Pass |
| HUD/EPA STANDARD |  | Floor Window sill |  |  | 40 g/ft2 250 g/ft2 |